## Slide 1: 18-613 Future of Computing
Milijana Surbatovich, Kiwan Maeng, Harsh Desai
Notes: …our work in developing a formal framework to reason about intermittent computing systems.

## Slide 2: Outline
Basics of intermittent computing
PL for intermittent computing
Systems for intermittent computing
Architectures for intermittent computing

## Slide 3: Batteryless Energy-harvesting Devices (EHDs) enable computing in inaccessible environments
Maintenance expensive or impossible
x
x := in()
y := x
z := y +5
Batteryless EHDs
x
x := in()
y := x
z := y +5

## Slide 4: Intermittent execution in energy harvesting devices
Energy Buffer
Harvester
Powers on as energy is available
Hardware platform
Notes: If energy is available, the device will charge, powering on when the buffer is full. The device will operate until access to the energy source is removed, such as …, and the buffer drains.

## Slide 5: Intermittent execution in energy harvesting devices
Energy Buffer
Harvester
Hardware platform
Volatile state clears, persistent state remains
Powers off at arbitrary program locations
Notes: At this point, the device powers off at an arbitrary program location for an arbitrary period of time. Any volatile state clears—typically including the program counter and registers--but persistent state remains. The device will remain off until energy becomes available again, repeating the cycle. Now, without runtime support, programs will not execute correctly.

## Slide 6: Mixed-volatility Memory
Volatile Memory loses state when the power turns off
  Register file, DRAM (traditional)
Non-volatile Memory keeps state when the power turns off
  Disk(traditional), Flash, STT-MRAM
Volatile
Non-volatile
Code
Program data
Registers
Peripherals
(Maybe) Stack

## Slide 7: Programs checkpoint to make progress
Power fail
Save state at checkpoints
Restore from save at reboots
If registers are cleared, program will restart from the beginning
Time
x := input()
i := i + 1
Power fail
…
x := input()
i := i + 1
data[i] := x
x := input()
i := i + 1
Power fail
x := input()
i := i + 1
i := i + 1
data[i] := x
Notes: For starts, since the program counter and registers clear on power failure, to make progress the runtime must save the execution context at checkpoints. The program will execute until power fails. On reboot, the program will continue executing from the last saved checkpoint instead of the beginning of the program, re-executing the partially executed section B.

## Slide 8: Checkpointing Methods
Just-in-time (JIT) checkpointing
Hardware to monitor voltage
Checkpoint on low power
Generally no re-execution
In-code checkpoints
Programmer or compiler adds
Re-execute from last checkpoint
x := input()
i := i + 1
data[i] := x
Low voltage!
x := input()
i := i + 1
data[i] := x
(More on this in next section)
(Focus of this section)

## Slide 9: Outline
Basics of intermittent computing
PL for intermittent computing
  Memory bugs caused by intermittence
  Formally Defining Correctness
  Correct checkpoint set
Systems for intermittent computing
Architecture for intermittent computing

## Slide 10: Systems must re-execute regions correctly
x := input()
i := i + 1
Must save starting value of i
Write-After-Read (WAR)
Incorrect dataflow
i := i + 1
data[i] := x
i
0
data
5
1
0
0
x
0
5
0
5
2
0
0
0
6
0
5
3
0
6
0
6
Skipped slot!
x := input()
i := i + 1
Correct Execution
i := i + 1
data[i] := x
i
0
data
5
1
0
0
x
0
5
0
5
2
0
0
0
6
0
5
1
0
0
0
6
0
5
2
6
0
0
6
State-of-the-art is to add WAR variables to the checkpoint set
K. Maeng, A. Colin, B. Lucia. Alpaca: Intermittent Execution without Checkpoints. OOPSLA ‘17
Notes: Unfortunately, this re-execution can cause bugs. One problem, which is largely solved by existing systems happens if there is a write-after-read dependence, such as when x reads y, and y is set to five. Re-executing the block introduced incorrect dataflow, and x reads the new value of y instead of the original. To be correct, the checkpoint needs to back up the original value of y as part of the execution context. One existing system…

## Slide 11: Input re-executions are not handled correctly
x := input()
Else z := 1
x := input()
If x > 5:
Incorrect behaviour!
y := 1
Else z := 1
Different on re-execution
Repeated-Input-Operation (RIO)
M. Surbatovich, L. Jia, B. Lucia. I/O Dependent Idempotence Bugs in Intermittent Systems. OOPSLA ‘19
x := input()
If x > 5:
y := 1
x
0
y
0
0
z
0
0
x
0
y
1
6
z
0
0
x
0
y
1
3
z
0
1
Notes: A problem that existing system largely don’t handle correctly is caused by repeating an input operation whose value is used by a branch. Consider if the branch is taken and y is set. The input could return a different value on re-execution, one that doesn’t take the branch and causes z to be set. Now both flags are set, which is incorrect. This problem was articulated in a paper from last OOPSLA, but we only provided a bug finding tool IBIS, not a correct runtime or formal specification.

## Slide 12: The need to formalize intermittent execution
No formal spec in existing works  systems subtly incorrect
Our correctness condition addresses both WAR and RIO problems, which no existing work has done

## Slide 13: Outline
Basics of intermittent computing
PL for intermittent computing
  Memory bugs caused by intermittence
  Formally Defining Correctness
  Correct checkpoint set
Systems for intermittent computing
Architecture for intermittent computing

## Slide 14: What does it mean to be correct?
Continuous execution specifies correct program behaviour
If intermittent execution is equivalent to a continuous execution, then it is correct
B
A
B
A
B
Intermittent Execution
Continuous
Execution
Notes: The intuition for correctness is that continuous executions are the specification of correct program behaviour. This means that a given intermittent execution is correct if there is some equivalent continuous execution. For a program to execute correctly, this must be true for all intermittent executions.

## Slide 15: Equivalence must hold for ALL intermittent executions of a program
If equivalence only holds for some executions, then a program is only sometimes correct, which is no good

## Slide 16: What makes equivalence difficult?
Equivalence: memory reads and memory state at checkpoints
B
A
B
Reboots don’t restore to the exact same state
B
A
Inputs cause different paths to be taken
B
B’
B
A
B
A
B
Intermittent Execution
Continuous
Execution
Many dimensions (time, energy…); this project looks at memory
Notes: Now, the traces don’t have to be the same, but rather *equivalent*. Equivalence means that memory reads and the memory state at each checkpoint or end of the program match that of some continuous execution. Two main challenges to reasoning about equivalence are that rebooting only reverts some values, so the restored state isn’t the same as at the checkpoint. Second, inputs can cause the program to take a different path on re-execution. These behaviours make equivalence difficult to reason since even a correct intermittent execution *will* have different memory at many points.

## Slide 17: Defining acceptable differences
17
Locations that don’t fit these conditions must be checkpointed!
B
A
B
Reboots don’t restore to the exact same state
B
A
Inputs cause different paths to be taken
B
B’
..so differing locations
should be written on re-execution (before being read)
..so differing locations should be written on all paths dependent on inputs
Notes: To reason if an execution is correct, we need to define the conditions where differences between the memories are acceptable and will resolve by the next checkpoint. The intuition is that to address the first challenge, all differing locations …, and because of inputs, these locations should be written on all paths that depend on inputs. Any locations that don’t fit these conditions *must* be checkpointed

## Slide 18: Many systems don’t satisfy this constraint
Exclusive May-Write (EMW) set: may-writes minus must-writes
Must be
Checkpointed
WAR
Conditionally written due to inputs
x
EMW
Y, Z
x := input()
If x > 5:
y := 1
Else z := 1
Meets Conditions
Notes: Going back to the example, x is written before being read, so it meets the conditions, but y and z must be checkpointed as neither is written on both paths. A system that only checkpoints WAR misses both these variables. To cover this difference, we define a new set that must be checkpointed, the exclusive may write set, which is may-write minus must must-writes

## Slide 19: Correctness Theorem
If all unsafe WAR and EMW variables are in the checkpointed set,
then an intermittent program will execute correctly
Checkpoint Set
B
A
B
A
B
Intermittent Execution
Continuous
Execution
Read Only
Meets Cond.
WAR
EMW
Safe
Notes: Defining EMW sets is a key piece needed to state our correctness theorem. Informally, it says that as long as all unsafe WAR and EMW are in the checkpoint set, then an intermittent program will execute correctly and equivalent to some continuous execution.

## Slide 20: How to reason precisely about intermittent execution?
Define a model language and system state (simple, but should include key features)
Define how executing commands changes the state
Show that no matter what command executes, the state
of the intermittent execution is related to a continuous execution

## Slide 21: Define a model language and system state
Programs are made of:
  Commands c ::=
  Instructions ι ::= … | x := e | checkpoint() | reboot
  Expressions e ::= x |v (e.g., int, bool) |
Particular to intermittence
Intermittent execution state:
is a record of the last checkpoint
N is non-volatile memory, a map of variables to values (x  3)
V is volatile memory
C is the command to execute

## Slide 22: Define how commands change state
B
A
B
Executing a command transitions a system from one state to another
Defines what happens at a checkpoint
List of locations to save
Copy only locations in the list
… do this for all commands.

## Slide 23: Prove the theorem
An intermittent execution is a sequence of state transitions
Show that after any transition, all memory locations either match the memory of the continuous execution or meet the conditions

## Slide 24: Take-aways
To build interesting applications, intermittent systems need to be robust to power failures of arbitrary position and duration
One challenge is that inputs cause bugs generally not handled by existing systems
Formalizing system behaviour and correctness definitions allow us to prove if a system is correct or not
Notes: So, the correctness definition is that any intermittent execution must be equivalent to some continuous execution. Differences in memory make this difficult to reason about, however, so the key piece of our formalism is two memory relations that define what differences are acceptable.